## Slide 1: CS/COE 0447
Negative Numbers, Arrays and Array Addressing
wilkie (with content borrowed from:
Jarrett Billingsley
Dr. Bruce Childers)

## Slide 2: Announcements
Lab 1 was due! Last Sunday!
  If you didn’t turn it in, first, that was silly of you.
  Because then you earned a Zero!
  But the lowest two labs will be dropped (because we all have lives, and sometimes homework doesn’t fit into that)
  Grades *should* be posted on Course Web (Blackboard)
The first midterm does seem like it is gonna be around where it is in the schedule.
  I’ll let you know what the topics are and some study material two weeks prior.
  So, don’t ask me what is on it now 
The first project will be assigned within the next two weeks
  It will be due AFTER the first midterm

## Slide 3: Lightning Recap
“Loads” move from? To? “Stores“ move from? To?
You are the CPU!
  That would be a good Halloween costume, right?
LW
I’m a CPU!
I’m invoking my right to use “Hipster wearing blank t-shirt” stock photos for educational purposes.

## Slide 4: Smaller Values
When your 32-bit cup doth not overfloweth… wait, no, that’s not right.

## Slide 5: MIPS ISA: load/store bytes/half-words
some values are tiny
to load/store bytes, we use lb/sb
to load/store 16-bit (half-word) values, we use lh/sh
These mostly look and work just like lw/sw, like:
lb t0, tiny # loads a byte into t0
sb t0, tiny # stores a byte into tiny
I said mostly… recall: how big are registers?
  So, what should go in those extra 16/24 bits then?
    ???

## Slide 6: Can I Get an Extension?
Sometimes you need to widen a number with fewer bits to more
zero extension is easy: put 0s at the beginning.
10012  to 8 bits  0000 10012
But there are also signed numbers which we didn't talk about yet… hmm

## Slide 7: Signed Numbers (sign-magnitude)
Seems like a good time to think about “negative” values.
  These are numbers that have nothing good to say.
Binary numbers have bits which are either 0 or 1.
  Well, yeah…
So what if we used one bit to designate “positive” or “negative”
  Called sign-magnitude encoding:
10100010 =
-34
00010110 =
22 (normal)

## Slide 8: Signed Numbers (problems)
Waaaaait a second.
  What is negative zero???
This encoding allows two different zeros.
  This means we can represent how many different values (8-bit)?
    2^8 – 1 (minus the one redundant value) = 255 (-127 … 0 … 127)
Sign-magnitude is a little naïve… let’s try a different approach…
10000000 =
-0
00000000 =
0

## Slide 9: Signed Numbers (1’s Complement)
Let’s borrow a technique from accounting and mechanical calculators: flip the dang bits.
OH COME ON (actually, this is better because math is easier)
  But this is really isn’t used that much.
11010100 =
-00101011 = -43
00000000 =
00000000 = 0
11111111 =
-00000000 = -0
00100110 =
00100110 = 38
😡

## Slide 10: Signed Numbers (2’s Complement)
This one, I promise, is juuuuust right.
  But it’s a little strange!
We’ll just make SURE there is only one zero:
So, we flip the bits… (1’s complement) and add one.
  Adding one makes sure our -0 is used for -1 instead!
Sure, it’s a little lopsided, but, hey, we get an extra number.
  But, hmm, but -4 doesn’t have a valid positive number.
    That’s the trade-off, but it’s for the best.
110
-2
101
-3
0
000
001
+1
010
+2
011
+3
111
-1
100
-4
0
000
001
+1
010
+2
011
+3
110
-1
101
-2
100
-3
111
1’s Complement
2’s Complement
😘

## Slide 11: Signed Numbers (2’s Complement)
Let’s look at the same bit patterns as before:
If the MSB is 1: Flip! Add one!
Otherwise: Do nothing! It’s the same!
11010100=
-00101011=-(43+1)=-44
00000000=
00000000= 0
11111111=
-00000000=-(0+1) =-1
00100110=
00100110= 38

## Slide 12: Signed Numbers (2’s Complement)
What happens when we add zeros to a positive number:
What happens when we add ones to a negative number:
00100110 = 38
0000000000100110 = ?
10100110 = ?
11111111110100110 =
-00000000001011001 = ?
-90
38
-90
Dang that’s cool!
10100110 = ?
-(01011001+1) = ?
-01011010 = ?
-90

## Slide 13: Can I Get an Extension? (Reprise)
Sometimes you need to widen a number with fewer bits to more
zero extension is easy: put 0s at the beginning.
10012  to 8 bits  0000 10012
But there are also signed numbers which we didn't talk about yet
  The top bit (MSB) of signed numbers determines the sign (+/-)
sign extension puts copies of the sign bit at the beginning
10012  to 8 bits  1111 10012
00102  to 8 bits  0000 00102

## Slide 14: E X P A N D
If you load a byte…
31 | 0 |  | 
00000000 | 00000000 | 00000000 | 00000000
10010000
31 | 0 |  | 
11111111 | 11111111 | 11111111 | 10010000
If the byte is signed… what should it become?
31 | 0 |  | 
00000000 | 00000000 | 00000000 | 10010000
If the byte is unsigned… what should it become?
lb does sign extension.
lbu does zero extension.
lbu (load byte unsigned) is USUALLY what you want to use!

## Slide 15: Truncation
31 | 0 |  | 
10100010 | 00001110 | 11111111 | 00000100
if we go the other way, the upper part of the value is cut off.
the sign issue doesn't exist when storing, cause we're going from a larger number of bits to a smaller number
  therefore, there are no sbu/shu instructions
31 | 0 |  | 
10100010 | 00001110 | 11111111 | 00000100
11111111 | 00000100
sh

## Slide 16: Arrays
Rice is great if you're really hungry and want to eat two thousand of something. – Mitch Hedberg, presumably talking about Arrays

## Slide 17: Strings, Arrays, etc
When we wanted to store 4-byte values…
  We split them up across consecutive bytes
What about a string?
  How is a string represented?
  How many bytes is a string?
    Might be thousands or millions of characters
Any array might be that big too!
The solution to storing it in memory is the same
  But how do you access these big things
    They don't fit in registers!
      ssssssssooooooooooooooooooooooooooo…

## Slide 18: What is an Array… ?
If we did this in C or Java:
byte[] arr = {1, 2, 3, 4, 5, ...};
In memory it might look like this
What memory address is arr[0] at?
  What about arr[1]?
  What about arr[2]?
  What about arr[3]?
If an array starts at memory address A…
  …then item at index i is at address…
  A + i ?
    Only if the array is holding individual bytes!
    Let’s take a deeper look.
Addr | Val
... | ...
F405 | 06
F404 | 05
F403 | 04
F402 | 03
F401 | 02
F400 | 01

## Slide 19: Let’s take a look at larger Arrays
So, if we did this: (“int” in Java is a 32-bit integer)
int[] arr = {1, 2, 3};
In memory it'd look like this
  Why are there all these 0s?
  What endianness is being used here?
    Which "end" of the 8-digit hex number is first?
What memory address is arr[1] at? arr[2]?
If an array starts at memory address A…
  …and each item is b bytes long…
  …then item i is at address A + (i × b)
    On the last slide, b happened to be 1
Addr | Val
F40B | 00
F40A | 00
F409 | 00
F408 | 03
F407 | 00
F406 | 00
F405 | 00
F404 | 02
F403 | 00
F402 | 00
F401 | 00
F400 | 01

## Slide 20: Arrays
If you wanna print all the values in an array:
for(int i = 0; i < length; i++)
print(data[i]);
Let's focus on ^ this bit ^ for now
data is an array of words, so how big is each item?
In this calculation, what is A ? b ? i ?
So what's the address calculation?
  Address of item i = data + (i * 4)
    Do you think you could convert that into assembly?
      Well we haven't done the loop yet…
        But we'll get to that

## Slide 21: Arrays in MIPS
The Practical Application of Two-Thousand Rice

## Slide 22: Defining Arrays in MIPS
First you need to make space for it just like a variable
  How did we write that variable?
myVar: .word 1 # int myVar = 1;
For a small array you can list all the values:
myArray: .word 1, 2, 3, 4
But for a big array, that would be annoying 
So you can write:
big_array: .word 0xBEEFC0DE:100
This fills the array with 100 copies of 0xBEEFC0DE
Notice how similar these look to variables
  (psst… that's cause there's not really any difference!)

## Slide 23: Load Address (la) instruction
Recall: Address of item i = arrayAddress + (i * b)
If the address calculation needs the address of the array…
  We've gotta get that address into a register right?
    Can't add something unless it's in registers!
This is what the la instruction does:
la t0, myArray # t0 = &myArray[0];
la means load address
  It doesn't load anything from memory.
  Only lw/lh/lhu/lb/lbu load from memory
  All the other "loads" (li, la) just "put a value in a register"
What it does: t0 now contains myArray's address

## Slide 24: Accessing Arrays: Let’s explore!
We want to print out the value in myArray[3].
What's the address calculation?
Now turn that into MIPS
  Let's come up with the instructions first
    And then decide which registers to use
  How do we put the address of myArray in a register?
  Now to translate the math
  Now we have the address; how do we get the value?
  How do we print it out?
If we want to store a value into the array…
  We just use a store instruction instead of a load.
See: array_ex1.asm

## Slide 25: How does the CPU know t0 holds an address?
WHAT DO YOU THINK
  IT DOESN’T!!
Addresses are just numbers too!!
Which means we can do math on addresses.
  Which we did.
  This is how arrays and strings work.
You can also have a variable whose value is an address.
  hey
  449 students
  what are these called
  pointers
    (& is like la, * is like lw/sw)

## Slide 26: Memory Alignment
We are exploring this a bit in Lab 2.
Let's remove the mul instruction
  "fetch address not aligned on word boundary"?
In MIPS, all memory accesses must be aligned
Alignment is just:
  The address of an n-byte value must be a multiple of n
    so for 4-byte words…
That's it, that's all, there's nothing more to it.
  It's not scary.
Addr | Val
F40B | 00
F40A | 00
F409 | 00
F408 | 03
F407 | 00
F406 | 00
F405 | 00
F404 | 02
F403 | 00
F402 | 00
F401 | 00
F400 | 01