## Slide 1: CS/COE 0447
Binary Arithmetic
wilkie (with content borrowed from:
Jarrett Billingsley
Dr. Bruce Childers)

## Slide 2: Binary Addition
Computers and 2 + 2 (well, 10 + 10, eh?)

## Slide 3: Adding in Binary
It works the same way as you learned in school
  Except instead of carrying at 1010, you carry at… 102!
    1 + 1 = 102 (210)
    1 + 1 + 1 = 112 (310)
Let's try it. (what are these in decimal?)
1011 0010
+0010 1111

## Slide 4: Formalizing “Addition”
For each pair of bits starting at the LSB,
  Add the two bits and the carry
  The low bit of the sum goes into the sum row
  The high bit of the sum is the carry for the next higher bit
This is the grade school algorithm
  Cause it's how you learned to add in grade school
What if there's a carry out of the biggest column??
  That’s ovvvvvverrrrfloooooow (remember that?)

## Slide 5: Ripple Adder (The Ole Classic)
When you add one place, you might get a carry out.
That becomes the carry in for the next higher place.
1 0 1 1 0 0 1 0
+0 0 1 0 1 1 1 1
Bit Bucket..?

## Slide 6: Looking at just a bit of this…
The resulting bit for each digit is dependent on the two input bits and the carry.
There are two outputs, however, a sum and a carry out.
1 0 1 1 0 0 1 0
+0 0 1 0 1 1 1 1
Bit Bucket..?
A
B
Cin
Cout
S

## Slide 7: 1-bit Adder
Let's try to come up with a truth table for adding two bits.
Each column will hold 1 bit.
We will ignore the carry input, for now.
A
B
Co
0
0
1
1
0
1
0
1
0
0
0
1
S
0
1
1
0

## Slide 8: Half-Truth Tables
What we just made was a half-adder.
It has a carry output but not a carry input
  (which might be useful for the lowest bit)
To make a full adder, we need 3 input bits.
A
B
Co
0
0
1
1
0
1
0
1
0
0
0
1
S
0
1
1
0
0
0
1
1
0
1
0
1
Ci
0
0
0
0
1
1
1
1
0
1
1
0
1
0
1
1

## Slide 9: The logic of it all
It looks a little messy, but it kinda makes sense if you think of it like this:
  It counts how many input bits are "1"
  Co and S are a 2-bit number!
If we look at the outputs in isolation:
  S is 1 if we have an odd number of "1s"
  Co is 1 if we have 2 or 3 "1s"
It's a little weird, but we can build this out of AND, OR, and XOR gates
A
B
Co
0
0
1
1
0
1
0
1
0
0
0
1
S
0
1
1
0
0
0
1
1
0
1
0
1
Ci
0
0
0
0
1
1
1
1
0
1
1
0
1
0
1
1

## Slide 10: Boolean Expression
S = ABCi + ABCi + ABCi + ABCi
Co = ABCi + ABCi + ABCi + ABCi
A
B
Co
0
0
1
1
0
1
0
1
0
0
0
1
S
0
1
1
0
0
0
1
1
0
1
0
1
Ci
0
0
0
0
1
1
1
1
0
1
1
0
1
0
1
1
S

## Slide 11: Sweeping it under the rug…
In programming, we use functions to be able to reuse code.
In hardware, we can group these 5 gates into a component.
Here's the symbol for a one-bit full adder.
+
B
A
Ci
Co
S
the inputs are like parameters
the outputs are like return values
now we don't have to care how it adds, just that it does

## Slide 12: PowerPoint REALLY wants me to do this
So, let’s make it happy so I can get on with my life
It’s always like “HEY LOOK AT THESE DESIGNS”

## Slide 13: Adding Longer Numbers
1-bit adders are cool and all, but, like, not very useful.

## Slide 14: Adding Longer Numbers
The resulting bit for each digit is dependent on the two input bits and the carry.
There are two outputs, however, a sum and a carry out.
1 0 1 1 0 0 1 0
+0 0 1 0 1 1 1 1
Bit Bucket..?

## Slide 15: Ripple Carry
If we want to add two three-bit numbers, we'll need three one-bit adders.
We chain the carries from each place to the next higher place, like we do on paper.
We have to split the numbers up like so:
+
B0
A0
S0
+
B1
A1
S1
+
B2
A2
S2
A2 | A1 | A0
B2 | B1 | B0
S2 | S1 | S0
+
C1
C2

## Slide 16: Negative Numbers
That first number… is negative… hmm
It works JUST FINE. It’s really neat actually…
1 0 1 1 0 0 1 0
+0 0 1 0 1 1 1 1
Bit Bucket..?

## Slide 17: Recall 2’s Complement
Let’s add them…
110
-2
101
-3
0
000
001
+1
010
+2
011
+3
111
-1
100
-4
2’s Complement
😘
1011 0010 : -78
+0010 1111 : +47
1110 0001 : -31

## Slide 18: Two’s Complement Addition
The great thing is: you can add numbers of either sign without having to do anything special!
1101
3
+-6
-3
3
+10
13
1
+1010
0011
0110
1001
1101
1
+1010
0011
0010
0011
to binary?
bit pattern for -6… positive 6?
flip!
+1
this is negative, so what is it? flip!
to decimal?
+1
3
the actual patterns of bits are the same. so how does the computer "know" whether it's
doing signed or unsigned addition?
-

## Slide 19
IT DOESN'T

## Slide 20: What.. Even.. Is.. Subtraction?
We could come up with a separate subtraction circuit, but…
Algebra tells us that x - y = x + (-y)
Negation means flip the bits and add 1
Flipping the bits uses NOT gates!
How do we add 1 without any extra circuitry?
  We use a full adder for the LSB, and when we're subtracting, set the "carry in" to 1.
+
~B0
A0
S0
+
~B1
A1
S1
+
~B2
A2
S2
C1
C2
Co
1

## Slide 21: What makes a good word size?
Can you think of an example of…
  100 of something?
  a million of something? a billion?
  a quintillion (1018)? more?
28 = 256, 216 ≅ 65,000, 232 ≅ 4 billion, 264 ≅ 18 quintillion
For a given word size, all the circuitry has to be built to support it
  64 1-bit adders
  128 wires going in
  64 wires coming out

## Slide 22: Gate Delay
Electrical signals can't move infinitely fast
Transistors can't turn on and off infinitely fast
Since each digit must wait for the next smaller digit to compute its carry…
  ripple carry is linear in the number of digits
This is a diagram of how the outputs of a 16-bit ripple carry adder change over time
  it's measured in picoseconds! so ~100ps total
But if we went to 32 bits, it'd take 200ps
  and 64 bits, 400ps...
There are more efficient ways of adding
  details, schmetails
(courtesy of Kate Temkin)

## Slide 23: Overflow
Revisiting What Happens When We Run Out of Dang Space

## Slide 24: How many bits?
If you add two 2-digit decimal numbers, what's the largest number you can get?
What about two 4-digit decimal numbers?
What about two 4-bit numbers?
What's the pattern of the number of digits?
  If you add two n-digit numbers in any base…
  The result will have at most n + 1 digits
That means if we add two 32-bit numbers…
  …we might get a 33-bit result!
  (It’s the 32 S output bits, and the last carry-out bit)
  if we have more bits than we can store in our number, that's overflow.
99
+99
198
9999
+9999
19998
1111
+1111
11110

## Slide 25: Detecting Overflow
For unsigned addition, it's easy
For an n-bit adder:
  just look at the Co of the MSB
  if it's 1, it's an overflow.
What about subtraction?
  shhh
25
+
B0
A0
S0
+
B1
A1
S1
+
B2
A2
S2
OVF

## Slide 26: Hmm, negative numbers
The signed number line looks like this:
Overflow occurs if we go off either end of the number line
In unsigned 3-bit arithmetic…
  1112 + 0012 = 10002
    that is, 7 + 1 = 8, which is too big.
But in signed 3-bit arithmetic…
  1112 + 0012 = 0
    because -1 + 1 = 0!
Same bit patterns, but different results.
  D etecting signed overflow is a bit more subtle…
110
-2
101
-3
0
000
001
+1
010
+2
011
+3
111
-1
100
-4

## Slide 27: Detecting Signed Overflow
If you add two numbers of different signs (negative and positive)…
  Is it possible to go off the ends of the number line?
    no!
    That always gets you closer to 0
If you add two numbers of the same sign, how do you know if you went off the end of the number line?
  If you add two positive numbers and get a negative number.
  If you add two negative numbers and get a positive number.
How do you check the signs of the three numbers?
  Do you think you could come up with a truth table? ;)

## Slide 28: Handling overflow
We could ignore it
  In MIPS: addu, subu
  This is usually a bad idea
    Your program is broken
  It's also the default in most languages, thanks C
We could fall on the floor - i.e. crash
  In MIPS add, sub
  Can be handled and recovered from
  But more complex
We could store that 33rd bit somewhere else

## Slide 29: Maybe the bit bucket is a real place…
Many other architectures do store this final 33rd (etc) bit.
  MIPS does not.
They have a "carry bit" register
  This can be checked by the program after an add/sub
This is very useful for arbitrary precision arithmetic
  If you want to add 2048-bit numbers, chain many 32-bit additions!