## Slide 1: CS/COE 0447
Data Representation: Binary, Hexadecimal, and Arbitrariness
wilkie (with content borrowed from:
Jarrett Billingsley
Dr. Bruce Childers)

## Slide 2: Binary
How to convert to and from Base-2 numeral systems

## Slide 3: Positional Number Systems
The numbers we use are written positionally: the position of a digit within the number has a meaning.
1,234
1s
10s
100s
1000s
100
101
102
103
How many digit symbols do we have in our number system?
  10: 0, 1, 2, 3, 4, 5 ,6 ,7, 8, 9
1 × 103 +
2 × 102 +
3 × 101 +
4 × 100
=
Most Significant
Least Significant

## Slide 4: Ranges of Representation
Suppose we have a 4-digit numeric display.
What is the smallest number it can show?
What is the biggest number it can show?
How many different numbers can it show?
  9999 - 0 + 1 = 10,000
What power of 10 is 10,000?
  104
With n digits:
  We can represent 10n numbers
  The largest number is 10n-1

## Slide 5: Numeric Bases
These 10s keep popping up… and for good reason
We use a base-10 (decimal) numbering system
  10 different digits, and each place is a power of 10
But we can use (almost) any number as a base!
The most common bases when dealing with computers are base-2 (binary) and base-16 (hexadecimal)
When dealing with multiple bases, you can write the base as a subscript to be explicit about it:
510 = 1012

## Slide 6: Let’s make a base-2 system
Given base B,
  There are B digit symbols
  Each place is worth Bi, starting with i = 0 on the right
  Given n digits,
    You can represent Bn numbers
    The largest representable number is Bn – 1
So how about base-2?

## Slide 7: Binary (base-2)
We call a Binary digIT a bit – a single 1 or 0
When we say an n-bit number, we mean one with n binary digits
27 26 25 24 23 22 21 20
1001 0110
128s 64s 32s 16s 8s 4s 2s 1s
1 × 128 +
0 × 64 +
0 × 32 +
1 × 16 +
0 × 8 +
1 × 4 +
1 × 2 +
0 × 1
= 15010
=
To convert binary to decimal: ignore 0s, add up place values wherever you see a 1.
MSB LSB

## Slide 8: Making Change
You want to give someone $9.63 in change, using the fewest bills and coins possible. How do you count it out?
Biggest to smallest
Most significant to least significant
WHERE COULD THIS BE GOING...
1
4
2
1
0
3
-$4=
$4.63
-50¢=
-10¢=
-0¢=
-3¢=
$0.63
$0.13
$0.03
$0.03
$0.00
$5× $1× 25¢× 10¢× 5¢× 1¢×__
Left:
$9.63
-$5=

## Slide 9: Converting Decimal to Binary
You want to convert the number 8310 to binary.
For each place from MSB:
If place value < remainder: 64 < 83, therefore:
  digit = 1 digit = 1
  remainder = remainder – place remainder = remainder–64 (83-64=19)
19 > 32, however, so:
  digit = 0 (remainder stays the same)
0
1
0
1
0
- 64 =
0
1
1
83
19
- 0 =
- 16 =
- 0 =
19
- 0 =
- 2 =
3
3
3
1
- 1 =
0
128s
64s
32s
16s
8s
4s
2s
1s
Left:
83
- 0 =

## Slide 10: Bits, bytes, nybbles, and words
A bit is one binary digit, and its unit is lowercase b.
A byte is an 8-bit value, and its unit is UPPERCASE B.
  This is why your 30 megabit (Mb/s) internet connection can only give you at most 3.75 megabytes (MB) per second!
A nybble (awww!) is 4 bits – half of a byte.
  Corresponds nicely to a single hex digit.
A word is the "most comfortable size" of number for a CPU.
When we say "32-bit CPU," we mean its word size is 32 bits.
  This means it can, for example, add two 32-bit numbers at once.
BUT WATCH OUT:
  Some things (Windows, x86) use word to mean 16 bits and double word (or dword) to mean 32 bits.

## Slide 11: Why binary? Whynary?
cause it's the easiest thing to implement. :P
arithmetic also becomes really easy (as we'll see in several weeks)
so, everything on a computer is represented in binary.
  everything.
  EVERYTHING.
  01000101 01010110 01000101 01010010 01011001 01010100 01001000 01001001 01001110 01000111 00101110
    (“EVERYTHING.”)

## Slide 12: Hexadecimal
How to convert to and from Base-16 numeral systems

## Slide 13: Shortcomings of Binary/Decimal
Binary numbers can get really long, really quickly.
  3,927,66410 = 11 1011 1110 1110 0111 00002
But nice "round" numbers in binary look arbitrary in decimal.
  10000000000000002 = 32,76810
This is because 10 is not a power of 2!
We could use base-4, base-8, base-16, base-32, etc.
  Base-4 is not much terser than binary
    e.g. 3,927,66410 = 120 3331 2323 00004
  Base-32 would require 32 digit symbols. Yeesh.
    They do, oddly, have their place… but not really in this context.
  Base-8 and base-16 look promising!

## Slide 14: Let’s make a base-2 16 system
Given base B,
  There are B digit symbols
  Each place is worth Bi, starting with i = 0 on the right
  Given n digits,
    You can represent Bn numbers
    The largest representable number is Bn – 1
So how about base-16?

## Slide 15: Hexadecimal or “hex” (base-16)
Digit symbols after 9 are A-F, meaning 10-15 respectively.
Usually we call one hexadecimal digit a hex digit. No fancy name :(
167 166 165 164 163 162 161 160
003B EE70
0 × 167 +
0 × 166 +
3 × 165 +
11 × 164 +
14 × 163 +
14 × 162 +
7 × 161 +
0 × 160 =
3,927,66410
=
To convert hex to decimal: use a dang calculator lol

## Slide 16: Converting from Binary to Hex
Four bits are equivalent to one hex digit.
Converting between them is easy!
Say we had this binary number:
11101111101110011100002
Starting from the LSB, divide into groups of 4 bits (put 0s before the first digits if there are leftovers). Then use the table.
0011 1011 1110 1110 0111 0000
Bin | Hex | Bin | Hex
0000 | 0 | 1000 | 8
0001 | 1 | 1001 | 9
0010 | 2 | 1010 | A
0011 | 3 | 1011 | B
0100 | 4 | 1100 | C
0101 | 5 | 1101 | D
0110 | 6 | 1110 | E
0111 | 7 | 1111 | F
3
B
E
E
7
0
0x
(this is common notation for hex, derived from the C language.)
know this table.

## Slide 17: Binary to Hex
1100
1010
0010
0000
0010
0001
0110
0100
4
C
A
2
0
2
6
1
0x4CA20261
32-bits! (Not so bad…)

## Slide 18: Base-8??
base-8, octal, used to be commonplace but isn't anymore
each octal digit (0-7) corresponds to three bits
  this made it a nice fit for 9-, 12-, 18-, and 36-bit machines
buuuut no one cares about octal anymore 
SORRY OCTAL
  it's okay, it has its revenge from time to time
  try this out in Java sometime: (leading zeroes mean octal, yikes!)
  System.out.println("012345 = " + 012345);

## Slide 19: The Powers of Two
Memorize at least the powers up to ~28 or 210.
  If you can't remember one, just add the previous one to itself.
These are the place values for binary, and they are also nice "round" numbers in binary and hex.
What is the largest number that an 8-bit value can hold? What is that in hexadecimal?
  255: 0xFF
How about a 16-bit value?
  65535: 0xFFFF
"0xFFFF" is kinda like "9999" in decimal.
  What happens if we go beyond that?
 | Dec | Hex
20 | 1 | 0x1
21 | 2 | 0x2
22 | 4 | 0x4
23 | 8 | 0x8
24 | 16 | 0x10
25 | 32 | 0x20
26 | 64 | 0x40
27 | 128 | 0x80
28 | 256 | 0x100

## Slide 20: Overflow
In computers, numbers are finite.
Let's say our 4-digit display was counting up: 9997, 9998, 9999…
What comes "next"?
  What does this "0000" really mean?
  It wrapped around.
This is overflow: the number you are trying to represent is too big to be represented.
Essentially, all arithmetic on the computer is modular arithmetic!
  This causes a lot of software bugs.

## Slide 21: What do we dooo???
if there's an overflow, that's bad right?
there are basically three options:
  store
  ignore
  fall on the floor and scream and cry about it
    (i.e. crash the program)
      (I* really struggled to come up with a rhyme)
each of these has pros and cons
we'll learn more about em later but keep them in your brainmeats
                * Jarrett did this, not me

## Slide 22: Summing it up (well, soon…)
everything's in binary, and hex is convenient shorthand
numbers don't really act like numbers?
actually, how does the computer know a number is a number?
how does it know how to add two numbers?
how does it know how to manipulate strings (for instance, text)?
how does it know if one pattern of bits is a string or a number or a video or a program or a file or an icon or

## Slide 23
IT DOESN'T

## Slide 24: Arbitrariness
How binary data is interpreted (or not. I mean who really knows?)

## Slide 25: What is means to be “arbitrary”
it means there's no reason for it to be that way.
we just kinda agree that it's how things are.
One of the biggest things I want you to know is:
What a pattern of bits means is arbitrary.
As a corollary:
The same pattern of bits can be interpreted many different ways.

## Slide 26: One bit pattern, many meanings
All information on computers is stored as patterns of bits, but…
How these bits are interpreted, transformed, and displayed is up to the programmer and the user.
11000100
-59
Signed integer
196
Unsigned integer
0xC4
Hexadecimal
Ä
Unicode
call nz
z80 instruction
R3G3B2 color

## Slide 27: The computer doesn’t know (or care)
when writing assembly (and C!) programs, the computer has no idea what you mean, cause nothing means anything to it
"my program assembles/compiles, why is it crashing?"
  cause the computer is stupid
    it's a big fast calculator
there's no difference between nonsense code and useful code
it's good at doing fun things with bit patterns
but don't confuse what it does with intelligence
every "smart" thing a computer does, it does because a human programmed it to act like that

## Slide 28: Next time…
Looking at how programs are represented
  Speaking of arbitrary…
    We will look at MIPS, tho, specifically
First taste of Assembly
  How values are stored, retrieved, manipulated.