## Slide 1: CS/COE 0447
Multiplication
wilkie (with content borrowed from:
Jarrett Billingsley
Dr. Bruce Childers)

## Slide 2: Multiplication
50 Ways to Move A Number

## Slide 3: Negative Re-enforcement?
Here's where most people would teach you Booth's Algorithm
There are a few problems with it:
  it's really complicated
  it's really confusing
  most importantly, literally no one uses it anymore
    and we haven't for decades
As far as I can tell, Booth's Algorithm is a waste of time used to torture architecture students and nothing more
  Although Booth’s Encoding can sometimes be useful
    Don’t ask me how though because I don’t know
Notes: - scientists put a group of 3 monkeys in a room with a ladder. at the top of the ladder was a banana.
- whenever any monkey tried to climb the ladder, the scientists sprayed them with a hose.
- eventually all the monkeys learned not to climb the ladder.
- then they replaced one monkey with a new one. new monkey tries to climb the ladder, but other 2 monkeys pull him down.
- eventually the new monkey learns not to climb the ladder from the other 2 monkeys.
- then they replaced another of the original monkeys… same thing.
- then they replaced the last original monkey… same thing.
- now they had three monkeys who had never been sprayed but nonetheless refused to go up the ladder.
  - "it's just how we've always done it."
  - "listen to your elders."
  - "do you really want to take the risk?"

## Slide 4: Multiplication by repeated addition
in A × B, the product (answer) is "A copies of B, added together"
6 × 3 =
1 | 2 | 3
18
how many additions would it take to calculate
500,000,000 × 2?
4 | 5 | 6
7 | 8 | 9
10 | 11 | 12
13 | 14 | 15
16 | 17 | 18

## Slide 5: Back to grade school
Remember your multiplication tables?
Binary is so much easier
If we list 0 too, the product logic looks awfully familiar…
✕ | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
1 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
2 | 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18
3 | 3 | 6 | 9 | 12 | 15 | 18 | 21 | 24 | 27
4 | 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32 | 36
5 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45
6 | 6 | 12 | 18 | 24 | 30 | 36 | 42 | 48 | 54
7 | 7 | 14 | 21 | 28 | 35 | 42 | 49 | 56 | 63
8 | 8 | 16 | 24 | 32 | 40 | 48 | 56 | 64 | 72
9 | 9 | 18 | 27 | 36 | 45 | 54 | 63 | 72 | 81
✕ | 1
1 | 1
A | B | P
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Notes: - it's an AND! (hey, we don't call it "logical product" for nothing.)

## Slide 6: Just like you remember
0101 =
× 0110 =
0000
0101
0101
0000___
0
00
0000000
You know how to multiply, riiiight?
5
× 6
0011110
30
these are partial products. how many additions are we doing?
wait, what operation are we doing here...?
Multiplicand
Multiplier
Notes: - for an n-bit multiplier, we have n partial products, and therefore O(n) additions.
- each partial product is shifted left one more place than the one above it.
- you do this in decimal too! each row of the partial product is multiplied by 10 (shifted left one place).

## Slide 7: Wait, why does this work?
What are we actually doing with this technique?
remember how positional numbers are really polynomials?
78×54
= 70×50 + 70×4 + 8×50 + 8×4
FOIL…
we're eliminating many addition steps by grouping them together.
we group them together by powers of the base.
= 78×50 + 78×4
Notes: - we're also "mashing together" some of the inner terms in each partial product.
- so even though this FOILing gives us 3 terms, we only have 2 partial products, since the middle term is split across 2 partial products.

## Slide 8: How many bits?
When we added two n-digit/bit numbers, at most how many digits/bits was the sum?
How about for multiplication?
When you multiply two n-digit/bit numbers, the product will be at most 2n digits/bits
So if we multiply two 32-bit numbers…
  we could get a 64-bit result! AAAA!
  if we just ignored those extra 32 bits, or crashed, we'd be losing a lot of info.
  so we have to store it.
99
× 99
9801
9999
× 9999
99980001
1111
× 1111
11100001
Notes: - when adding two n-bit numbers, we could get an n+1-bit result.
- technically if you multiply an m-bit number by an n-bit result then the product can be (m+n) bits, but if m = n (commonly), then it's 2n.

## Slide 9: 32-bit multiplier
Here’s the first algorithm.
  It’s the Elementary School One
For each bit in our multiplier,
  Look at the current first bit of the multiplier
  If it is a “1”, add the multiplicand to the result
  Shift left our result by 1
  Shift right multiplier by 1
Begin
Result =0;
N=0;
End
Test bit 0 of multiplier
N<32?
Multiplier0=1
Multiplier0=0
Yes, repeat!
No, Terminate
Multiplier = Multiplier >> 1
N = N + 1
Result = Result + Multiplicand
Multiplicand = Multiplicand << 1
Notes: - for an n-bit multiplier, we have n partial products, and therefore O(n) additions.
- each partial product is shifted left one more place than the one above it.
- you do this in decimal too! each row of the partial product is multiplied by 10 (shifted left one place).

## Slide 10: What is this O.o
It’s an ALU!
  Arithmetic and Logic Unit
What does it do?
  It adds and subtracts numbers
  It also does logical operations OR, AND, NOR, NAND, etc.
What about overflows?
  Let’s not worry about those right away 
But how does it work??
  Soon…
32
32
32
operation

## Slide 11: Hardware multiplier – Version 1
Multiplicand (64 bits)
64
64
64
Result (64 bits)
Multiplier (32 bits)
Control
Shift left
Shift right
LSBit
Write
Operation
In version 1 of the multiplier, the ALU and the registers Multiplicand and Result are 64-bit registers
Notes: - we're also "mashing together" some of the inner terms in each partial product.
- so even though this FOILing gives us 3 terms, we only have 2 partial products, since the middle term is split across 2 partial products.

## Slide 12: Example 1
Let’s exemplify by multiplying 86 by 66. The result should be 5676.
01010110
× 01000010
00000000
+ 01010110_ 010101100
+ 01010110 _ 001011000101100

## Slide 13: Hardware multiplier – Version 1
0000000001010110
16
16
16
0000000000000000
0100001 0
Control
Shift left
Shift right
LSBit
Write
Operation
(add)
Begin
Init
Add
Shift
End
Bit 0?
N=8?
Iteration
0000000010101100
0010000 1
0000000010101100
0000000101011000
0001000 0
0000100 0
0000001010110000
0000010101100000
0000010 0
0000001 0
0000101011000000
0001010110000000
0000000 1
0001011000101100
0010101100000000
0000000 0
0101011000000000
0000000 0
Result
(example with 8 bit registers: 01000010 x 01010110 = 00010110 00101100)
Multiplier
Multiplicand

## Slide 14: Let’s think about this
There is a relative movement between the Multiplicand and the Result!
  The shift
  What if we moved the result to the right instead?
0000
+ 0101
01010
0000
+ 0000 0000
01010
+ 0101
011110
011110
+ 0000
0011110
0000
+ 0101
01010
0000
+ 0000 0000
01010
+ 0101
011110
011110
+ 0000
0011110

## Slide 15: Let’s think about this
We also see that in every iteration, the value of a bit is set to it’s final value.
  Starting in the LSB moving to the MSB
And the top bit is always 0
  So there is no carry!
  0+0=0 and 0+1=1
So we are only operating on 32 bits
  Therefore we only need a 32-bit adder

## Slide 16: Hardware multiplier – Version 2
In version 2 of the multiplier, the ALU and the Multiplicand register only need to be 32-bit registers
32
32
32
Control
Shift right
Shift right
LSBit
Write
Operation (add)
Result
Result (64 bits)
Multiplier (32 bits)
Multiplicand (32 bits)

## Slide 17: Hardware multiplier – Version 2
01010110
8
8
8
0000000000000000
0100001 0
Control
Shift right
Shift right
LSBit
Write
Operation (add)
Begin
Init
Add
Shift
End
Bit 0?
N=8?
Iteration
0010000 1
0000000000000000
0001000 0
0000100 0
0000010 0
0000001 0
0000000 1
0000000 0
0000000 0
Result
0101011000000000
0010101100000000
0001010110000000
0000101011000000
0000010101100000
0000001010110000
0101100010110000
0010110001011000
0001011000101100
(example with 8 bit registers: 01000010 x 01010110 = 00010110 00101100)

## Slide 18: Let’s think about this
Both the Result and the Multiplier register are shifted right identically.
Every time we add a new bit to the result, we lose a bit in the Multiplier
What if we store the Multiplier on the less significant part of the Result register?
  This would reduce the amount of space required by multiplication

## Slide 19: Hardware multiplier – Version 3
In version 3 of the multiplier, the Multiplier register is removed, its value is stored in the least significant half of the result.
32
32
32
Control
Shift right
LSBit
Write
Operation (add)
Result
Multiplicand (32 bits)
Result (64 bits)
Multiplier (32 bits)

## Slide 20: Hardware multiplier – Version 3
01010110
8
8
8
0000000001000010
Control
Shift right
LSBit
Write
Operation (add)
Begin
Init
Add
Shift
End
Bit 0?
N=8?
Iteration
0000000000100001
Result
0101011000100001
0010101100010000
0001010110001000
0000101011000100
0000010101100010
0000001010110001
0101100010110001
0010110001011000
0001011000101100

## Slide 21: How (and why) MIPS does it
MIPS has two more 32-bit registers, HI and LO. if you do this:
mult t0, a0
then HI = upper 32 bits of the product and LO = lower 32 bits
to actually get the product, we use these:
mfhi t0 # move From HI (t0 = HI)
mflo t1 # move From LO (t1 = LO)
the mul pseudo-op does a mult followed by an mflo
MIPS does this for 2 reasons:
  multiplication can take longer than addition
  we'd otherwise have to change two different registers at once
if you wanted to check for 32-bit multiplication overflow, how could you do it?
Notes: - you could use mfhi to get the upper 32 bits and see if it's nonzero.
- if all the upper bits are 0, then the result fits comfortably in 32 bits.
- if all the upper bits are 1, then the result is negative… and may be either 32 or 33 bits… so more checks… ugh…

## Slide 22: Signed multiplication
Multiplication can be mean and negative, too

## Slide 23: Grade school (but like, 5th, instead of 3rd)
if you multiply two signed numbers, what's the rule?
A | B | P
3 | 5 | 15
3 | -5 | -15
-3 | 5 | -15
-3 | -5 | 15
A | B | S
+ | + | +
+ | - | -
- | + | -
- | - | +
Product
Sign
if the signs of the operands differ, the output is negative.
Notes: - you may or may not recognize this logic as exclusive OR.

## Slide 24: Don't repeat yourself
We already have an algorithm to multiply unsigned numbers
Multiplying signed numbers is exactly the same (except for the signs)
So why not use what we already made?
long prod = unsigned_mult(abs(A), abs(B));
if(sgn(A) == sgn(B))
return prod;
else
return –prod;
Notes: - abs(x) = {-x if x < 0; x otherwise}
- sgn(x) = {-1 if x < 0; 1 if x > 0; 0 otherwise}