## Slide 1: CS/COE 0447
Implementing Logic:
Teaching the Machine to “think”
wilkie (with content borrowed from:
Jarrett Billingsley
Dr. Bruce Childers)

## Slide 2: What's electricity?
(for fun section)

## Slide 3: In your orbit
p+
e-
here's a proton. it has a positive charge
here's an electron. it has a negative charge
it kinda goes around
the proton in an orbit*
*narrator: that was not true.
protons sit still while electrons can move around

## Slide 4: Opposites attract…
p+
e-
p+
e-
opposite charges attract
two of the same charge repel
here's electricity. here it is
but protons are kinda stuck, so…

## Slide 5: Lots of fish electrons in the sea
here's a solid piece of metal
the atoms are in a fixed structure
but some of the electrons are free to move around
right now, the charges are balanced: same number of positive and negative
let's knock it out of whack

## Slide 6: Two moles is company, three's a crowd
let's shove more electrons in
aaa
noo
packing more electrons in leads to two things:
1. this metal is now negatively charged
2. the electrons are now closer together meaning they're less happy

## Slide 7: Carousel of unhappiness
and then give them a (difficult) way out
and then have something which will squeeze them back together again
well now you have electricity
wire
if we shove some down a wire
wire
we'd like to get off mister bones wild ride

## Slide 8: Watch em go
voltage measures electron unhappiness
current measures how many electrons per second are moving past a point
low
high
low
high
and that's electricity

## Slide 9: Logic Basics
Transistors n’at

## Slide 10: Transistors
A transistor is like a little valve, or switch
The input, output, and control are all single bits
The bits are represented as voltages (maybe 3.3V = 1, 0V = 0)
it connects its input to its output if control is a 1
input
output
control
now just put 3 billion of them together! who said EE was hard?

## Slide 11: Two Types of MOS Transistor
Metal Oxide Semiconductor transistors come in two varieties:
X
Y
G
G = 1
G = 0
ON
OFF
Y
X
Y
X
X
Y
G
G = 0
G = 1
Y
X
Y
X
“P” Type
“N” Type

## Slide 12: Gates
We can combine transistors in interesting ways to make gates
A gate implements one of the basic boolean logic functions
Let's start with the simplest: the NOT gate
this little bubble means "invert"
A
Q
A is the input
Q is the output

## Slide 13: Time to bundle up
If we want to, say, NOT a 32-bit value, we can draw it like:
32
32
It's a lot nicer than drawing 32 wires with 32 NOT gates
Logisim calls these wire bundles
  It doesn't draw the slashes and numbers though…

## Slide 14: NOT (With MOS Transistors)
AKA an “Inverter”
Input value “A” manipulates transistors and output “Q”
Voltage goes to ground ( ) unless it goes to Q
“high” voltage == “1"
3.3V
X
~0.0V
A | Q
0 | 1
1 | 0
A
Q

## Slide 15: NAND (MOS)
A | B | Q
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
NAND gate
AB

## Slide 16: AND (MOS)
A
Q
B
AND gate
A | B | Q
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
AB

## Slide 17: NOR (MOS)
A | B | Q
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
NOR gate
A
Q
B
A+B

## Slide 18: OR (MOS)
A
Q
B
OR gate
A | B | Q
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A+B

## Slide 19: AND, OR, and… XOR?
we know about AND and OR, but what's XOR?
A
Q
B
AND gate
A
Q
B
OR gate
A
Q
B
XOR gate
A | B | Q
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A | B | Q
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
eXclusive OR means "one or the other, but NOT BOTH."
A | B | Q
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
AB A+B AxB

## Slide 20: AND (multiple inputs)
If you have more than 2 inputs… you can just concatenate:
A
Q’
B
AND gate
Q’
Q
C
AND gate
A | B | C | Q
0 | 0 | 0 | 0
1 | 0 | 0 | 0
0 | 1 | 0 | 0
1 | 1 | 0 | 0
0 | 0 | 1 | 0
1 | 0 | 1 | 0
0 | 1 | 1 | 0
1 | 1 | 1 | 1

## Slide 21: AND and/or OR
Combining logic is just a matter of combining logic gates:
Look at when Q is “1”
OR each of those by the AND of each term:
ABC + ABC
A | B | C | Q
0 | 0 | 0 | 0
1 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 1 | 0 | 0
0 | 0 | 1 | 0
1 | 0 | 1 | 0
0 | 1 | 1 | 1
1 | 1 | 1 | 0

## Slide 22: AND and/or OR
ABC + ABC
B
A
Q
C
A | B | C | Q
0 | 0 | 0 | 0
1 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 1 | 0 | 0
0 | 0 | 1 | 0
1 | 0 | 1 | 0
0 | 1 | 1 | 1
1 | 1 | 1 | 0

## Slide 23: If you give an electrical engineer a NAND gate…
Sum up: If a NOT gate is after an AND gate, you get a NAND gate:
This kind of gate has a cool property: it's universal
  In other words, you can build an entire computer with NANDs (or NORs)
  Think how to build a NOT from a NAND (Then build an AND, etc)
But this isn't how real circuits are designed, at least not anymore
Digital logic courses use them cause NAND gate chips are cheap
But in Logisim, we have infinite gates for free :D
Use the kind of gate you need for the situation at hand